Cockpit dimensions
- Width of cockpit leg room
  - KH: 1.5 cm * 32 = 48 cm
  - RK: 1.45 cm * 32 = 46.4 cm
  - Ejection seat: https://www.britmodeller.com/forums/index.php?/topic/235109451-martin-baker-mk10-seat-dimensions/: 47 cm
  - => chosen 48 cm to have a bit of margin between the seat and the cockpit (plus a nicer number)

---
Blender inherited
Factor to reduce dimensions is ca. 0,23

---
VTH = HUD
Blender:
The material for the VTH is canvas_transparent and has an alpha of 0.9. If you set it to a higher values, then the whole canvas gets green. The lower the value is set, the less visible the text/lines get.
The width of the inner side of the VTH:
Blender file -5: 13.8 cm
RK: 0.4*32 = 12.8 cm
KH (glass): 0.4*32 = 12.8 cm
From pictures it looks like the whole middle section is about 1/3 of cockpit leg-room – inluding outer stuff of hud -> 16 cm, maybe hud glass structure sides are 1 cm -> 14 cm
Blender file inherited: 0.74 cm * 0,23 = 17 including out4er stuff of hud
=> stick with -5 blender file: 13,8 cm

---
- The average of the orange lines is 90 degs – i.e. the photo is representative for horizontal
- The VTH glass has an angle of 45 deg respective to horizontal (green line)
- The VTH body has an angle of 13 degs respective to horizontal (red line)
- The lower part of the cockpit body has an angle of 28 degs (yellow line)

---
Camera
Camera body width: 11 cm/11.6 = 0,95*13,8 = 13,11 -> 13 cm